## Slide 1: CHEM 545/546 Group Project
Members: Omkar Bhambure, Yueyang Chen, Rachel Gebhart, Isaac Kretzmer

## Slide 2: Project Objectives
Goal: Analyze characteristics of SEM images
Deliverables:
  Average particle size (float radius)
  Particle size distribution (float average, histogram)
  Measure of how spherical/elliptical the particles are (density plot)
  Stretch: some measure of irregularity/roughness (we’ll figure this out later)
Inputs:
  *.TIFF from FEI XL830 SEM

## Slide 3: How We Start
Use Edge detection to separate particles
  Fit curve splines
  Count particles
OpenCV Package
  Open Source Python Package for Image Processing (MIT License)
  Multiple methods of edge detection available for use
    Sobel
    Canny
    Laplace

## Slide 4: Example

## Slide 5: Canny Edge Detection
Smooth image using Gaussian filter
  Noise filtering
Find intensity gradients
  First derivatives
Remove non-maximum peaks
  Compare to nearby gradients
Mark weak edges
  Caused by true edges, noise, and color
Hysteresis edge tracking
  Remove edges caused by noise and color
Pros
  Non-maximum suppression and weak edge marking extract edges well
Cons
  Fails with very noisy images, requires parameter tuning

## Slide 6: Laplacian Edge Detection
1D image
First order
Derivative
Second order
Derivative
Pros:
Easy to calculate (One pass calculation)
Cons:
Sensitive to noise
Need to apply filter before/after the edge detection
Examples:

## Slide 7: Sobel Edge Detection
Sobel operator is a joint Gaussian smoothing and differentiation operation
You can specify the direction of the derivative
Size of the Kernal can be changed
Pros:
  Edges seem thick and bright
Cons:
  High Computational time
  It is very noisy.